| AUTOMATIC CONTROLS AND TOLERANCE RECORD FOR PORTLAND CEMENT CONCRETE PLANTS | Wisconsin Department of Transportation |
| --- | --- |
| DT1926 2/2006 (Replaces EC253) | Region |
|  |  |  |  | Project | Contract |
| ZERO INTERLOCK |  |  |
| Scale | Capacity (lbs.) | Spec. Tol. .3% | Tolerance (lbs.) | Name of Road | County |
| Aggregate |  | x.003 |  |  | Highway Number |
| Aggregate |  | x.003 |  | Location |
| Aggregate |  | x.003 |  | Contractor |
| Cement |  | x.003 |  | Inspected by | Date |
| Material | Interlock | Designated Bin Weight | Accumulative Designated Batch Weight | Actual Scale Reading | ACT. Tol. Lbs. | SPEC. Tol. Lbs. | ACT. Tol. % | SPEC. Tol. % |
|  | Zero |  |  |  |  |  |  |  |
|  | Underweight |  |  |  |  |  |  | 1.5 |
| Aggregate |  |  |  |  |  |  |  |  |
|  | Overweight |  |  |  |  |  |  | 1.5 |
|  | Zero |  |  |  |  |  |  |  |
|  | Underweight |  |  |  |  |  |  | 1.5 |
| Aggregate |  |  |  |  |  |  |  |  |
|  | Overweight |  |  |  |  |  |  | 1.5 |
|  | Zero |  |  |  |  |  |  |  |
|  | Underweight |  |  |  |  |  |  | 1.5 |
| Aggregate |  |  |  |  |  |  |  |  |
|  | Overweight |  |  |  |  |  |  | 1.5 |
|  | Zero |  |  |  |  |  |  |  |
|  | Underweight |  |  |  |  |  |  | 1.5 |
| Aggregate |  |  |  |  |  |  |  |  |
|  | Overweight |  |  |  |  |  |  | 1.5 |
| Portland Cement | Zero |  |  |  |  |  |  |  |
|  | Underweight |  |  |  |  |  |  | 1.0 |
|  | Overweight |  |  |  |  |  |  | 1.0 |
| INTERLOCK CHECK | HOPPER DISCHARGE |  | CEMENT | AGGREGATE |
|  |  | Open while hopper inlet is opened? | Yes | No | Yes | No |
|  |  | Open if batch is not within tolerance? | Yes | No | Yes | No |
|  | HOPPER INLET | Open before hopper is empty? | Yes | No | Yes | No |
|  |  | Open while hoper discharge is open? | Yes | No | Yes | No |

REMARKS